lsusb
Execute the above command to see if ID 2e8a:0003 Raspberry Pi RP2 Bootthis line exists. If not, please check the USB cable (remember to hold down the BOOT key before connecting)

## 4. Configuration and testing
Tip
The installation method of accelerometer dependent package is as follows:
Tip
It is recommended to use SSH tools such as MobaXterm_Personal to operate
Tip
This step is for 非FLY上位机, if you are a Fly-πor Geminiseries, you don’t need to perform it! ! !
Execute the following three commands in sequence to install the accelerometer dependency package.
sudo apt update
sudo apt install python3-numpy python3-matplotlib libatlas-base-dev
~/klippy-env/bin/pip install matplotlib numpy
Please note that depending on the performance of the CPU it may take a lot of time, up to 10-20 minutes. Please wait patiently for the installation to complete. In some cases, the installation may fail if the motherboard has too little RAM.
Open printer.cfg and add accelerometer configuration
[mcu adxl]
serial: /dev/serial/by-id/usb-Klipper_rp2040_XXXXXXXXXXXXXXXXXXXXX
### 查询usb固件id是：ls -l /dev/serial/by-id/
### 把/dev/serial/by-id/usb-Klipper_rp2040_XXXXXXXXXXXXXXXXXXXXX替换查询到的id

##ADXL345加速度计
[adxl345]
cs_pin: adxl:gpio9
spi_software_sclk_pin: adxl:gpio10
spi_software_mosi_pin: adxl:gpio11
spi_software_miso_pin: adxl:gpio12

[resonance_tester]
accel_chip: adxl345
probe_points:
    100, 100, 20 # 此坐标为你需要测量的位置，一般为热床中间
- Save and restart after modifying the configuration
- Execute on consoleACCELEROMETER_QUERY
- Multiple accelerometers can be specified to test a certainACCELEROMETER_QUERY CHIP=bed
- If an error occurs, please check the wiring and configuration.
- The normal output is as shown below

- This way you can measure resonance.
- Remember to put everything back in place
- Test the X axis TEST_RESONANCES AXIS=Xand change the Y axis to Y as well.
Tip
Notice! If the printer vibrates too violently during the test, please press Emergency Stop or Send M112to stop it in time.
If it is too high, accel_per_hzthe vibration will become severe, and it can be reduced appropriately.
[resonance_tester]
accel_chip: adxl345
accel_per_hz: 50 # 默认值为75
probe_points: ...
## 5. Automatic calibration
- klipper supports automatic calibration
- Remember to put everything back in place
- SHAPER_CALIBRATEAfter executing this command, the printer will start to automatically calibrate X, Y
- Executed after calibration is complete SAVE_CONFIGto save data
- It can also be used SHAPER_CALIBRATE AXIS=Xto automatically calibrate an axis,
- After each axis calibration is completed, the data must be saved before calibrating the next one.

The calibration process may take a long time, please be patient.