# Calibration procedures

I am following the methods described here : https://teachingtechyt.github.io/calibration.html
# Frame check

The Y roller wheels needed some tightening as well as the X belt. Nothing else was loose
# PID autotune for the head
Using Klipper console : PID_CALIBRATE HEATER=extruder TARGET=205
New PID values
KI = 1.304
KP = 26.213
KD = 131.721
OriginalPID values
KI = ?
KP = ?
KD = ?
# PID Autotune for both Heat beds (Using Klipper)
The original printer.cfg did not use PIE for bed temperature control but rather Watermark (On Off) !! I could see variations of +-1.5 degrees
Using Klipper console : PID_CALIBRATE HEATER=heater_bed TARGET=60
Using Klipper console : PID_CALIBRATE HEATER=heater_bed1 TARGET=60
Bed New PID values
KI = 70.0
KP = 2.0
KD = 600.0
Bed1 New PID values
KI = 73.0
KP =1.15
KD = 1158.0
# Extruder E-steps

Asked for 100 mm of wire got 92 mm !! 8% error. Since the web site procedure does not seem to apply to Klipper I will just change the extruder rotation_distance: 29 # was 31.4
rotation_distance: was 31.4
rotation_distance: now 29
With this value if I ask for 100mm I get
# Probe Accuracy
Probe resolution seems to be 0.0025 mm 0.0001 “

No heat at home position

09:58:53  $ PROBE_ACCURACY
09:58:53  // PROBE_ACCURACY at X:141.000 Y:98.000 Z:2.988 (samples=10 retract=3.000 speed=10.0 lift_speed=10.0)
09:58:54  // probe at 141.000,98.000 is z=-0.015000
09:58:55  // probe at 141.000,98.000 is z=-0.015000
09:58:56  // probe at 141.000,98.000 is z=-0.015000
09:58:57  // probe at 141.000,98.000 is z=-0.015000
09:58:58  // probe at 141.000,98.000 is z=-0.015000
09:58:59  // probe at 141.000,98.000 is z=-0.012500
09:59:00  // probe at 141.000,98.000 is z=-0.012500
09:59:01  // probe at 141.000,98.000 is z=-0.012500
09:59:02  // probe at 141.000,98.000 is z=-0.012500
09:59:03  // probe at 141.000,98.000 is z=-0.012500
09:59:03  // probe accuracy results: maximum -0.012500, minimum -0.015000, range 0.002500, average -0.013750, median -0.013750, standard deviation 0.001250

Head at 205 bed at 60

10:00:12  $ SET_HEATER_TEMPERATURE HEATER=extruder TARGET=205
10:00:17  $ SET_HEATER_TEMPERATURE HEATER=heater_bed TARGET=60
10:00:21  $ SET_HEATER_TEMPERATURE HEATER=heater_bed1 TARGET=60
10:08:35  $ PROBE_ACCURACY
10:08:35  // PROBE_ACCURACY at X:141.000 Y:98.000 Z:2.988 (samples=10 retract=3.000 speed=10.0 lift_speed=10.0)
10:08:36  // probe at 141.000,98.000 is z=0.090000
10:08:37  // probe at 141.000,98.000 is z=0.090000
10:08:38  // probe at 141.000,98.000 is z=0.087500
10:08:39  // probe at 141.000,98.000 is z=0.087500
10:08:40  // probe at 141.000,98.000 is z=0.090000
10:08:41  // probe at 141.000,98.000 is z=0.092500
10:08:42  // probe at 141.000,98.000 is z=0.092500
10:08:43  // probe at 141.000,98.000 is z=0.095000
10:08:44  // probe at 141.000,98.000 is z=0.092500
10:08:45  // probe at 141.000,98.000 is z=0.0950010:08:45  // probe accuracy results: maximum 0.095000, minimum 0.087500, range 0.007500, average 0.091250, median 0.091250, standard deviation 0.002562

So the probe absolute trigger position is affected by temperature. A difference of +0.01050 mm between cold and hot Hot probe. The hot probe detects 0.01050 mm higher !!

# Bed levelling
1- Using the pendant set the temps to PLA preset
2- Wait for temp to stabilize
3- Start autoleveling
Since the probe is affected by temperature let’s do the autoleveling at room temp and save it. Then let’s set temperatures to the working temps for our filament (nozzle and both beds). Then let’s home the machine and then do a Z_OFFSET calibration using the 4 mils feeler gauge and save it.
# Pressure advance calibrations

Using instructions at https://www.klipper3d.org/Pressure_Advance.html
square_tower.gcode @ Neptune4/Calibrations/Pressure Advance

2023-09-12 09:43:11

Elegoo Black PLA
Chinese knockoff CHT 0.4 mm brass nozzle

In non vase mode offset = 18.87

So Pressure advance 0 + 18,87 * 0.005 = 0.0944

The original pressure advance for the Elegoo nozzle was set from the factory at 0.022 !!

12 Sept 2023
Pressure advance calibration was done and confirmed for Elegoo black PLA at 200 mm/s

Custom Prusa End gcode macro was modified to turn of Nozzle and bed (both) heating

A Calibration torture test was printed (Ringing on X) filament streams and bad small detail resolution. Dimentional precision was quite good.