# Hot head PID feedback

Original PID values KI = KP = KD =
New PID values = KI = KP = KD =
# Heat bed PID feedback
Bed Original PID values No PID just watermark
Bed New PID values = KI = KP = KD =
Bed1 Original PID values No PID just watermark
Bed1 New PID values = KI = KP = KD =
# Pressure advance calibrations

Using instructions at https://www.klipper3d.org/Pressure_Advance.html
square_tower.gcode @ Neptune4/Calibrations/Pressure Advance

2023-09-12 09:43:11

Elegoo Black PLA
Chinese knockoff CHT 0.4 mm brass nozzle

In non vase mode offset = 18.87

So Pressure advance 0 + 18,87 * 0.005 = 0.0944

The original pressure advance for the Elegoo nozzle was set from the factory at 0.022 !!

# Probe Accuracy

Probe resolution seems to be 0.0025 mm 0.0001 “

No heat at home position

09:58:53  $ PROBE_ACCURACY
09:58:53  // PROBE_ACCURACY at X:141.000 Y:98.000 Z:2.988 (samples=10 retract=3.000 speed=10.0 lift_speed=10.0)
09:58:54  // probe at 141.000,98.000 is z=-0.015000
09:58:55  // probe at 141.000,98.000 is z=-0.015000
09:58:56  // probe at 141.000,98.000 is z=-0.015000
09:58:57  // probe at 141.000,98.000 is z=-0.015000
09:58:58  // probe at 141.000,98.000 is z=-0.015000
09:58:59  // probe at 141.000,98.000 is z=-0.012500
09:59:00  // probe at 141.000,98.000 is z=-0.012500
09:59:01  // probe at 141.000,98.000 is z=-0.012500
09:59:02  // probe at 141.000,98.000 is z=-0.012500
09:59:03  // probe at 141.000,98.000 is z=-0.012500
09:59:03  // probe accuracy results: maximum -0.012500, minimum -0.015000, range 0.002500, average -0.013750, median -0.013750, standard deviation 0.001250

Head at 205 bed at 60

10:00:12  $ SET_HEATER_TEMPERATURE HEATER=extruder TARGET=205
10:00:17  $ SET_HEATER_TEMPERATURE HEATER=heater_bed TARGET=60
10:00:21  $ SET_HEATER_TEMPERATURE HEATER=heater_bed1 TARGET=60
10:08:35  $ PROBE_ACCURACY
10:08:35  // PROBE_ACCURACY at X:141.000 Y:98.000 Z:2.988 (samples=10 retract=3.000 speed=10.0 lift_speed=10.0)
10:08:36  // probe at 141.000,98.000 is z=0.090000
10:08:37  // probe at 141.000,98.000 is z=0.090000
10:08:38  // probe at 141.000,98.000 is z=0.087500
10:08:39  // probe at 141.000,98.000 is z=0.087500
10:08:40  // probe at 141.000,98.000 is z=0.090000
10:08:41  // probe at 141.000,98.000 is z=0.092500
10:08:42  // probe at 141.000,98.000 is z=0.092500
10:08:43  // probe at 141.000,98.000 is z=0.095000
10:08:44  // probe at 141.000,98.000 is z=0.092500
10:08:45  // probe at 141.000,98.000 is z=0.095000
10:08:45  // probe accuracy results: maximum 0.095000, minimum 0.087500, range 0.007500, average 0.091250, median 0.091250, standard deviation 0.002562

So a difference of +0.01050 mm between cold and hot Hot probe detects 0.01050 mm higher !!
12 Sept 2023
Pressure advance calibration was done and confirmed for Elegoo black PLA at 200 mm/s

Custom Prusa End gcode macro was modified to turn of Nozzle and bed (both) heating

A Calibration torture test was printed (Ringing on X) filament streams and bad small detail resolution. Dimentional precision was quite good.